## Slide 1
Demo – week 9
András Pásztor
08.12.2017

## Slide 2
Past
Architectural Engineer

## Slide 3
Electronic assembling plant
Past
Facility Engineer

## Slide 4
Past
Facility and Property Manager

## Slide 5
Long time ago…
Programing and Electronics

## Slide 6
Timing
STM32F7

## Slide 7
Timing
The problem was…
How to calculate the setup of a TIMx timer to have
1 Hz pulse?

## Slide 8
Timing
Discover the documentation of MCU
STM32F7

## Slide 9
Timing
Discover the documentation of MCU
Datasheet
Reference Manual
General-purpuse Timer Cookbook
STM32F7

## Slide 10
Timing
MCU Block Diagram
Datasheet

## Slide 11
Timing
Clock Tree
Reference Manual

## Slide 12
Timing
Block Diagram

## Slide 13
Timing
Clock Tree

## Slide 14
Timing
Calculate
How to calculate the setup of the TIM1 timer to have 1 Hz pulse?
PLL is set to 216 MHz
TIM1 is on APB2

## Slide 15
Timing
Calculate
PLL 216 MHz
AHB_PRESC 1
APB2_PRESC 8
If (APBx_PRESC = 1)
then x1
else x2
TIM base clock = PLL / AHB_PRESC / APB2_PRESC x 2
TIM base clock = 216 Mhz / 1 / 8 x 2 = 54 MHz

## Slide 16
Timing
Calculate
TIM base clock = 216 Mhz / 1 / 8 x 2 = 54 MHz
TIM base clock 54 000 000 Hz
TIM prescaler 6750
TIM period 8000
TIM clock = 54 000 000 Hz / 6750 / 8000 = 1 Hz

## Slide 17
Take time to find and check the manuals
Take Home Message

## Slide 18
András Pásztor
Thank you for your attention